SPECIFICATION

Section 07900

2 HOUR RATED (UL)

ISO-FLEX WINGED

EXPANSION JOINT SEALING SYSTEM

## PART 1 – GENERAL

  - WORK INCLUDED

The work shall consist of furnishing and installing 2 hour fire rated expansion joints in accordance with the details shown on the plans and the requirements of the specifications.

  - RELATED DOCUMENTS

Drawings and provisions of the contract, including General and Supplementary Conditions apply to this section.

  - QUALITY ASSURANCE

- Work under this section shall be performed by an applicator approved by the manufacturer.  The manufacturer shall evidence in writing that the applicator designated to perform the work is qualified to install the specified systems.

- Prequalification of bidders:  Submit proposed subcontractors to the engineer prior to bid.  Qualification criteria shall include compliance with 1.03-A above.  Specifier retains absolutely the right to reject any applicator or manufacturer submitted.

- A site inspection shall be made by the approved applicator prior to commencing installation of the specified system, for the purpose of reviewing related conditions affecting performance requirements of this specification.

- All products described in this section must be used with adequate personal protection.  Refer to the Material Safety Data Sheet that accompanies each product shipment for detailed health and safety information prior to use.

  - SUBMITTALS

- A detailed statement describing the expansion joint sealing system to be installed including typical cross section details with pertinent dimensioning.  Approved Installers shall prepare and submit details of all special conditions to the manufacturer for review and approval prior to installation.

- Provide UL listing certification that the fire rated joint assembly has been tested and approved by Underwriters Laboratories in accordance with UL 2079 (ASTM E119), class II.

- Manufacturer’s written acceptance and approval of the intended system applicator is required.

## PART 2 – PRODUCTS

  - MATERIALS

- Provide 2 hour (UL) fire rated watertight expansion joint system that is capable of accommodating multi-directional movement.  The system shall be composed of a preformed thermoplastic seal with integral “wings” in combination with a fire barrier blanket that are to be cast into a pre-established blockout via an elastomeric concrete nosing.

The thermoplastic seal shall be sized to accommodate the total range of movement as dictated by the specifier at each joint location.  Sizing shall be done in such a way as to ensure that the “winged” seal will never exceed its nominal dimension.

Furnish the Iso-Flex Winged Expansion Joint Sealing System Series “J” at locations requiring 2 hour fire rating and watertightness, as manufactured by LymTal Intl., and as indicated on the drawings.

  - COMPONENT PROPERTIES

- Thermoplastic Winged Seal

Provide seal as specified and indicated on the contract drawings.  Seal design shall incorporate integral “wings” with factory-punched holes on each side, which interlocks the seal into the elastomeric concrete header material.  Seal material shall meet the following physical properties indicated below:

### PHYSICAL PROPERTIES –  “J” SYSTEM

Physical Properties		ASTM Test Method		Requirements

Shore A Hardness			D-2240			67 +- 3

Tensile Strength			D-412				1010 psi

Ultimate Elongation		D-412				450%

100% Modulus			D-412				420 psi

Tear Strength			D-642				138 lb/in

Tension Set			D-412				10%

Compression Set			D-395				23% @ 77( F

168 hours							36% @ 212( F

Brittle Point			D-746				-76( F

- Elastomeric Concrete

Provide manufacturer’s elastomeric concrete header material consisting of two liquid components and pregraded aggregate.

PHYSICAL REQUIREMENTS FOR ISO-FLEX 900

ELASTOMERIC CONCRETE

Tensile Strength		ASTM D-412		7 days		1680 psi

Tensile Elongation	ASTM D-412		7 days		240%

Hardness, Durometer A	ASTM D-2240	7 days		90 ± 3

Tear Resistance, min	ASTM D-624		7 days		195 lbs/inch

Compressive Strength

5% Deflection		ASTM D-695				1442 psi

Resilience, %		ASTM D-695				96%

Packaging	One US gallon with half gallon activator and one 60# container of aggregate

Shelf Life	One year from date of manufacture

- Bonding Agent

All concrete that will come in contact with the winged seal must be primed with Iso-Flex Primer #10.

- Fire Barrier

The fire barrier system shall be an engineered flexible 3 lb. density textile material with a fiberglass matt facing containing unexpanded vermiculite. The fire barrier is engineered to accommodate expansion and contraction.

- Accessories

Provide necessary and related parts including preformed or fabricated wall mount plates with appropriate anchors and sealant for complete installation.

- Fabrication

Joint seal directional changes shall be factory welded wherever possible according to field measurements and drawings on centerline provided by the contractor.  Site welding, where required, can be carried out only after suitable instruction by the expansion joint manufacturer.

  - Finishes

- Thermoplastic winged seal shall be supplied in standard color:  Black

- Elastomeric Concrete Header shall be supplied in standard color:  Black.

PART 3 – EXECUTION

  - General

All work shall be installed in strict accordance with the system manufacturer’s recommendations employing trained installers utilizing proper tools and equipment and working under the direct supervision of a technically competent and experienced supervisor.

  - Preparation

- The contractor shall provide properly formed, solid blockouts with clean, sound concrete free of voids and honeycombs, and in accordance with the dimensions detailed in the drawings.

- The contractor shall clean the concrete blockout of all contaminants by sandblasting immediately prior to ire rated expansion joint system installation.  Concrete form release agents, laitance, surface dirt and rust, old sealants and other surface treatments, as well as anything which would inhibit the bond of Iso-Flex 900 Elastomeric Concrete System must be removed from the blockout surface prior to beginning the installation of the system.

- Areas adjacent to the joint must be masked with tape to assure clean joint lines.

- The blockout area must be completely dry for the application of the Iso-Flex 900 Elastomeric Concrete System.  Concrete must be fully cured (28 days) prior to placement of the Iso-Flex 900.  Blockouts requiring the use of patching compounds must be cured for 72 hours prior to placement of the Iso-Flex header system.

- The blockouts must be made to the dimensions and elevations shown on the standard system drawings.  Deviations from these dimensions will not be allowed without the written consent of LymTal Intl.

- The fire barrier shall be unpackaged and unrolled in the area adjacent to the expansion joint gap. As the fire barrier is installed it is folded in half and inserted into the expansion joint gap opening. The fire barrier will be recessed into the joint gap in order to allow installation of the J Series Winged expansion joint. seal.

- The winged seal element shall be unpackaged and laid in a relaxed position to relieve any temporary coiling from shipment packaging prior to placement; the winged flaps of the gland element shall be wiped with an acceptable non-petroleum solvent cleaner such as Xylol (Xylene).

- Work shall not proceed under adverse weather conditions or when temperatures are outside the manufacture’s recommended ranges.

  - Installation

The installation of the expansion joint system shall be completed in strict accordance with the manufacturer’s recommendations.

  - Clean and Protect

Protect the Fire Rated Iso-Flex Winged Expansion Joint Sealing System during construction.  Heavy construction vehicles will not be permitted to cross the joint without specific and written permission by the engineer.  Subsequent damage to the expansion joint system shall be repaired at the contractor’s expense.

-end-